## Slide 1
GRADUATE RESEARCH PRESENTATION
Optimization of a Heterogeneous Edge AI Inference Pipeline
TDA4VM SoC | C7x DSP | Quantization
Emre Doğan & Yavuz Selim Kızıltaş Istanbul Technical University | Hacettepe University

## Slide 2
I. INTRODUCTION & PROBLEM
Deploying real-time vision on low-power hardware requires deep optimization beyond simple model conversion.

## Slide 3
The TDA4VM integrates specialized processing cores :
Hardware Constraints: On-chip shared memory capacity
is limited, and DDR bandwidth can become a bottleneck for large tensor transfers.
Accuracy Constraints: The quantized model should remain close to the FP32 baseline in terms of detection accuracy.
Real-Time Constraints:: The pipeline should satisfy deterministic timing requirements and avoid memory-related delays.
→
→
→
CONSTRAINTS
Toolchain Constraints: Model deployment relies on the TIDL toolkit and TI Processor SDK, which support a defined subset of neural network operators in optimized INT8 mode
→

## Slide 4
The TDA4VM integrates specialized processing cores :
ARM Cortex-A72: Dual-core 64-bit Arm Cortex-A72 microprocessor subsystem at up to 2.0GHz
C7x DSP: floating point, vector DSP, up to 1.0GHz, 80 GFLOPS, 256 GOPS
C66x DSP: Two C66x floating point DSP, up to 1.35GHz, 40GFLOPS, 160GOPS
→
→
→
TARGET HARDWARE: TI TDA4VM SOC
ARM Cortex-R5F: Six Arm Cortex-R5F MCUs at up to 1.0GHz
→

## Slide 5
The TDA4VM integrates specialized accelerators :
MMA: Deep-learning matrix multiply accelerator (MMA), up to 8 TOPS (8b) at 1.0GHz
VPAC: Vision Processing Accelerators with Image Signal Processor (ISP) and multiple vision assist accelerators
3D GPU: PowerVR Rogue 8XE GE8430, up to 750MHz, 96GFLOPS, 6Gpix/sec
→
→
→
TARGET HARDWARE: TI TDA4VM SOC
DMPAC: Depth and Motion Processing Accelerators
→

## Slide 6
Custom-designed interconnect fabric supporting near max processing entitlement Memory subsystem:
1MB shared L2 cache per dual-core Cortex-A72 cluster, 32KB L1 DCache and 48KB L1 ICache per Cortex-A72 core
Memory: 8MB of on-chip L3 RAM with ECC and coherency
→
→
TARGET HARDWARE: TI TDA4VM SOC
LPDDR4: External Memory Interface (EMIF) module with ECC
→
16K I-Cache, 16K D-Cache, 64K L2 TCM per six Six Arm Cortex-R5F MCUs
→

## Slide 7
Primary Objective
Minimize end-to-end latency to satisfy deterministic 30 FPS real-time requirements in ADAS/Robotics/Defence Ind.
Hardware Constraints
Strict 8MB on-chip shared memory budget and finite DDR bandwidth for large tensor transfers.
Accuracy Target
Maintain quantized model accuracy within ε range of the baseline FP32 performance.
SYSTEM REQUIREMENTS & GOALS

## Slide 8
Base Model Selection
Edge AI Studio
ONNX/TFLite model format
TIDL Configuration
Adjusting the ONNX/TFLite model for TIDL.
Quantization and Calibration settings
Model Compilation
Cross compilation using by Edge AI TIDL Tools on x86 PC
IMPLEMENTATION
Host Emulation
Model test on a TIDL-RT Host Emulation
Board Integration
Moving compiled artifacts to the TDA4VM Board
TDA4VM Inference
Main application tasks and inference pipeline implementation

## Slide 9
Efficiency vs Accuracy
Quantization reduces memory footprint by 4x and compute energy significantly. Our calibration strategy ensures mAP degradation remains < 2% for most lightweight architectures.
Leveraging TIDL Import Tools for optimal per-layer scaling.
INT8 PRECISION IMPACT

## Slide 10
SYSTEM DATAFLOW
Heterogeneous pipeline distributes tasks across cores to maximize parallel execution:
ARM: Camera capture and resizing.
C7x+MMA: Intensive TIDL INT8 Inference.
C66x: Post-processing (NMS, decoding).
SRAM: Shared double-buffering.
→
→
→
→

## Slide 11
Decision Variable | Definition | Constraint
ci ∈ C | Processing Unit (ARM, C7x, C66x) | Hardware Operator Support
si ∈ {0, 1} | Memory Placement (DDR, MSMC) | Σ mi ≤ Mshared
Si | Scheduling/Tiling Order | Ttotal ≤ Tdeadline
OPTIMIZATION MODEL

## Slide 12
PTQ INT8
TIDL-based Post-Training Quantization. Calibrated conversion of FP32 weights to 8-bit integers to leverage MMA performance.
Memory Placement
Greedy allocation policy for MSMC SRAM. High-reuse activation tensors are prioritized for on-chip storage to reduce DDR stalls.
Stage Overlap
Double-buffering and DMA-based prefetching. Overlapping memory movement with DSP compute to hide data transfer latency.
THREE PILLARS OF OPTIMIZATION

## Slide 13
Model | Input Resolution | Activation Mem. | Shared RAM Fit | mAP (COCO)
YOLOX-Nano | 416 x 416 | ~2-3 MB | FULL | 25.8
YOLOX-Tiny | 416 x 416 | ~3-4 MB | FULL | 32.8
SSD-MobileNetV2 | 300 x 300 | ~3 MB | FULL | 22.1
EfficientDet-Lite0 | 320 x 320 | ~3.4 MB | FULL | 26.3
YOLOX-S | 640 x 640 | 6-8 MB | MARGINAL | 40.5
CANDIDATE MODEL BENCHMARKS
→ mAP in COCO is an object detection metric that provides measurement of both detection accuracy and localization quality

## Slide 14
W1-2
Setup & Baseline Selection
W3-4
Quantization & TIDL Import
W5-6
Pipeline & DMA Integration
W7-8
Profiling & Optimization
IMPLEMENTATION TIMELINE

## Slide 15
End-to-End Latency
(ms):
The total time from frame
capture to final detection output.
Throughput (FPS):
Sustained frames processed per second
under continuous inference load.
Energy Efficiency:
Performance-per-watt or platformlevel
power/performance indicators, if measurable.
REQUIREMENTS EVALUATION
Detection Accuracy (mAP):
Standard object detection
mAP evaluated for both FP32 and INT8 versions of the
model.
Memory/Transfer Efficiency:
Evidence of reduced
costly DDR traffic or improved use of shared on-chip
memory where measurable.

## Slide 16
Questions & Discussion
Thank you for your attention.
Optimization of a Heterogeneous Edge AI Inference Pipeline Istanbul Technical University | Hacettepe University